28 July 2009

SPECIFICATIONS FOR COMMONLY USED FERTILIZERS

(Tailored to the requirement of TCE for procurement)

1.  N,P and K Fertilizers

- UREA (Free flowing)

- UREA (Granular)

- AMMONIUM SULPHATE

- CALCIUM AMMONIUM NITRATE (CAN)

- SINGLE SUPERPHOSPHATE (SSP) (Powdered)

- SINGLE SUPERPHOSPHATE (SSP) (Granular)

- TRIPLE SUPERPHOSPHATE (TSP)

- POTASSIUM CHLORIDE/ MURIATE OF POTASH (MOP) (Crystalline powder)

- POTASSIUM CHLORIDE/ MURIATE OF POTASH (MOP) (Granular)

- POTASSIUM SULPHATE/SULPHATE OF POTASH (SOP)

- DIAMMONIUM PHOSPHATE (DAP)

- NPK COMPLEX 15-15-15

- NPK COMPLEX 17-17-17

- NPK COMPLEX 19-19-19

______

UREA (Free flowing)

- Moisture content by weight: maximum 1%

- Total nitrogen content by weight (on dry basis): minimum 46%

- Biuret content by weight: maximum 1.5%

- Particle size: Not less than 90% of the material shall pass through 2.8 mm IS sieve and be retained on 1 mm IS sieve.  Not more than 5% shall be below 1 mm IS sieve

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

UREA (Granular)

NOTE: Only when specially requested (for machine application) as it is slightly more 	expensive than free flowing Urea

- Moisture content by weight: maximum 1%

- Total nitrogen content by weight (on dry basis): minimum 46%

- Biuret content by weight: maximum 1.5%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and be retained on 2 mm IS sieve. Not more than 5% shall be below 1 mm IS sieve

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

AMMONIUM SULPHATE

- Moisture content by weight: maximum 1%

- Total nitrogen content by weight (on dry basis): minimum 20%

- Free acidity (as H2SO4) by weight: maximum 0.025%

- Sulphur (as S) by weight: minimum 23%

- Particle size: Not less than 90% of the material shall pass through 2.8 mm IS sieve and be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm IS sieve

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

CALCIUM AMMONIUM NITRATE (CAN)

- Moisture content by weight: maximum 1%

- Total nitrogen content by weight (on dry basis): minimum 26%

- Ammoniacal nitrogen by weight: 50% of total nitrogen

- Nitrate nitrogen by weight: 50% of total nitrogen

- Calcium and/or magnesium carbonate by weight: minimum 18%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm IS sieve

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# SINGLE SUPERPHOSPHATE (SSP) (Powdered)

- Moisture content by weight: maximum 12%

- Free phosphoric acid (as P2O5) by weight:  maximum 4%

- Water soluble phosphate (as P2O5) by weight: minimum 15.8%

- Sulphur (as S) by weight: minimum 11%

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# SINGLE SUPERPHOSPHATE (SSP) (Granular)

NOTE: Price may be slightly higher than powdered material. Quotations may be asked for both types and decision to be taken based on availability and price.

- Moisture content by weight: maximum 5%

- Free phosphoric acid (as P2O5) by weight:  maximum 4%

- Water soluble phosphate (as P2O5) by weight: minimum 15.8%

- Sulphur (as S) by weight: minimum 11%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and shall be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# TRIPLE SUPERPHOSPHATE (TSP)

- Moisture content by weight: maximum 5%

- Free phosphoric acid (as P2O5) by weight:  maximum 3%

- Total phosphates (as P2O5) by weight: minimum 46%

- Water soluble phosphate (as P2O5) by weight: minimum 42.5%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and shall be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# POTASSIUM CHLORIDE/ MURIATE OF POTASH (MOP) (Crystalline powder)

- Moisture content by weight: maximum 0.5%

- Water soluble potash content (as K2O) by weight: minimum 60%

- Sodium (as NaCl) by weight: maximum 3.5%

- Particle size: Not less than 65 % of the material shall pass through 1.7 mm IS sieve and be retained on 0.25 mm IS sieve

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# POTASSIUM CHLORIDE/MURIATE OF POTASH (MOP) (Granular)

NOTE: Price may be slightly higher than crystalline powder material. Quotations may be asked for both types and decision to be taken based on availability and price.

- Moisture content by weight: maximum 0.5%

- Water soluble potash content (as K2O) by weight: minimum 60%

- Sodium (as NaCl) by weight: maximum 3.5%

- Magnesium (as MgCl2) by weight: maximum 1%

- Particle size: Not less than 90% of the material shall pass through 3.35 mm IS sieve and be retained on 1 mm IS sieve. Not more than 5% should be below 1 mm size.

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# POTASSIUM SULPHATE/SULPHATE OF POTASH (SOP)

- Moisture content by weight: maximum 1.5%

- Potash content (as K2O) by weight: minimum 50%

- Total chlorides (as Cl) by weight: maximum 2.5%

- Sodium (as NaCl) by weight: maximum 2%

- Sulphur (as S) by weight: minimum 17.5%

- Particle size: Not less than 65 % of the material shall pass through 1.7 mm IS sieve 	and be retained on 0.25 mm IS sieve

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with 	polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project 	No., P.O. No. and final destination

# DIAMMONIUM PHOSPHATE (DAP)

- Moisture content by weight: maximum 1.5%

- Total nitrogen content by weight (on dry basis): minimum 18%

- Neutral ammonium citrate soluble phosphate (as P2O5) content by weight: minimum 46%

- Water soluble phosphate (as P2O5) content by weight: minimum 41%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm size

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cos.

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

NPK COMPLEX 15-15-15

- Moisture content by weight: maximum 1.5%

- Total nitrogen content by weight (on dry basis): minimum 15%

- Neutral ammonium citrate soluble phosphate (as P2O5) content by weight: minimum 15%

- Water soluble phosphate (as P2O5) content by weight: minimum 12%

- Water soluble potash (as K2O) content by weight: minimum 15%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm size

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# NPK COMPLEX 17-17-17

- Moisture content by weight: maximum 1.5%

- Total nitrogen content by weight (on dry basis): minimum 17%

- Neutral ammonium citrate soluble phosphate (as P2O5) content by weight: minimum 17%

- Water soluble phosphate (as P2O5) content by weight: minimum 13.6%

- Water soluble potash (as K2O) content by weight: minimum 17%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm size

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

# NPK COMPLEX 19-19-19

NOTE:  All other NPK complex grades will follow the same rule, particularly water soluble phosphate content should be 85% (minimum) of the neutral ammonium  citrate soluble phosphate content.

- Moisture content by weight: maximum 1.5%

- Total nitrogen content by weight (on dry basis): minimum 19%

- Neutral ammonium citrate soluble phosphate (as P2O5) content by weight: minimum 19%

- Water soluble phosphate (as P2O5) content by weight: minimum 16.2%

- Water soluble potash (as K2O) content by weight: minimum 19%

- Particle size: Not less than 90% of the material shall pass through 4 mm IS sieve and be retained on 1 mm IS sieve. Not more than 5% shall be below 1 mm size

- Packing: Packed in 50 kg (dry) capacity woven polypropylene bags with polyethylene inner lining. 4% empty bags to be supplied at no extra cost

- Each bag to guarantee minimum product weight (net) as specified on the bag

- Marking: FAO logo, product name, active ingredient(s), net and gross weight, Project No., P.O. No. and final destination

2. Micronutrient Fertilizers

# ZINC SULPHATE

- Zinc (as Zn) content by weight: minimum 21%

- Sulphur (as S) content by weight: minimum 10%

- Lead (as Pb) content by weight: maximum 0.003%

- Copper (as Cu) content by weight: maximum 0.1%

- Magnesium (as Mg) content by weight: maximum 0.5%

- Cadmium (as Cd) content by weight: maximum 0.0025%

- Arsenic (as As) content by weight: maximum 0.01%

- Matter insoluble in water by weight: maximum 1%

- pH: not less than 4

- Form: free flowing powder

# CHELATED Zn, AS Zn-EDTA

- Zinc content (expressed as Zn) by weight in the form of Zn-EDTA complex: minimum 12%

- Lead (as Pb) content by weight: maximum 0.003%

- pH: 6.0 – 6.5

- Form: free flowing crystalline/powder

# MANGANESE SULPHATE

- Manganese (as Mn) content by weight: minimum 30.5%

- Sulphur (as S) content by weight: minimum 17%

- Lead (as Pb) content by weight: maximum 0.003%

- Copper (as Cu) content by weight: maximum 0.1%

- Magnesium (as Mg) content by weight: maximum 2%

- Matter insoluble in water by weight: maximum 1%

- pH: not less than 3.75

- Form: free flowing powder

# BORAX (SODIUM TETRABORATE)

- Boron (as B) content by weight: minimum 10.5%

- Lead (as Pb) content by weight: maximum 0.003%

- Matter insoluble in water by weight: maximum 1%

- pH: 9.0-9.5

- Form: free flowing powder

# COPPER SULPHATE

- Copper (as Cu) content by weight: minimum 24%

- Sulphur (as S) content by weight: minimum 12%

- Soluble iron and aluminium compounds (expressed as Fe) content by weight: maximum 0.5%

- Lead (as Pb) content by weight: maximum 0.003%

- Matter insoluble in water by weight: maximum 1%

- pH: not less than 3

- Form: free flowing powder/granular

# FERROUS SULPHATE

# Ferrous iron (as Fe) content by weight: minimum 19%

- Sulphur (as S) content by weight: minimum 10.5%

- Free acid (as H2SO4) content by weight: maximum 1%

- Ferric iron (as Fe) content by weight: maximum 0.5%

- Lead (as Pb) content by weight: maximum 0.003%

- Matter insoluble in water by weight: maximum 1%

- PH: not less than 3.5

- Form: free flowing powder

# CHELATED IRON, AS Fe-EDTA

- Iron content (expressed as Fe) by weight in the form of Fe-EDTA complex: minimum 12%

- Lead (as Pb) content by weight: maximum 0.003%

- pH: 5.5 – 6.5

- Form: free flowing crystalline/powder

AMMONIUM  MOLYBDATE

- Molybdenum (as Mo) content by weight: minimum 52%

- Lead (as Pb) content by weight: maximum 0.003%

- Matter insoluble in water by weight: maximum 1%

- pH: 5.0-5.5

- Form: free flowing crystalline/powder

3. Rock Phosphate (RP)/Phosphate Rock (PR) for Direct Application

- Total phosphates (as P2O5) content by weight: between 15-35% depending on source

- Cadmium (as Cd) content by weight: maximum 27 mg/kg of RP

- Particle size: Not less than 90% of the material shall pass through 0.15 mm IS sieve and the balance shall pass through 0.25 mm IS sieve

.

4. Organic Manures

Quality of organic manures vary widely, depending on the materials used. However, basic criteria to consider suitability of the material as a nutrient source are:

- Organic matter content by weight: minimum 30%

- Organic carbon content by weight: minimum 12%

- Total nutrients (N+ P2O5+ K2O) content by weight: minimum 5%

Subject to doubt and availability of analytical facilities, contents of following heavy metals should be checked:

- Arsenic (As) content by weight: maximum 10 mg/kg

- Cadmium (Cd) content by weight: maximum 5 mg/kg

- Cromium (Cr) content by weight: maximum 50 mg/kg

- Copper (Cu) content by weight: maximum 300 mg/kg

- Lead (Pb) content by weight: maximum 100 mg/kg