## Slide 1: Evaluation of alternative cell lines for the isolation of FMDV
Ashley Gray, Valerie Mioulet, Britta Wood, Elizabeth Reid, Lissie Henry, Barsha Thapa, Donald King

## Slide 2: Scope
Virus isolation remains key component in FMDV diagnostics
Cells currently used in the WRL:
  Primary bovine thyroid: expensive, labour intensive, require experienced staff
  IB-RS-2 pig kidney: Persistently infected with CSF and therefore, requirement for biosafety provisions
Purpose: Investigate the FMDV sensitivity of other continuous cell lines for use in diagnostics

## Slide 3: Sensitivity comparisons
Figure 2: The LFBK-αVβ6 cell line produced consistently higher viral titres (logTCID50) (average + SD) than IB-RS-2 and ZZ-R for isolate HKN 1/2015 type O (CATHAY topotype). The number of titrations conducted to-date are shown on each bar (n).
Chart: logTCID50
| IB-RS-2 | ZZ-R | LFBK-αVβ6 | Cell line
Virus Strain HKN 1/2015 | 5.8 | 6.9 | 8.2
n=2
n=3
n=4

## Slide 4: Future work
Sensitivity comparisons using clinical samples
Validation required for ISO/IEC 17025 accreditation
Development of a continuous BTY cell line expressing high levels of αVβ6 integrin receptor
Acknowledgement
With thanks to L. Rodrigues and M. LaRocco, Plum Island, USDA/ARS, for providing the LFBK- αVβ6 cell line.