## Slide 1: Measuring carbon and water footprints in pineapple value chains
Introductory session

## Slide 2: Content
  Challenges and opportunities in the pineapple sector
  What carbon and water footprint measurements are and why these are important
  Measuring carbon and water footprints in the pineapple sector
  Reducing greenhouse gas (GHG) emissions and water impacts in pineapple value chains

## Slide 3
1.
Current challenges in the pineapple sector

## Slide 4: Current challenges in the pineapple sector
Cultivation is climatically vulnerable in tropical regions.
Fast growing international demand for pineapple.
Rising requirements from export markets to report on environmental impacts and GHG emissions.
Important source of economic growth, livelihoods, food and nutrition security for producing countries.

## Slide 5
Current challenges in the tropical fruit sector

## Slide 6
2.
What are carbon and water footprint measurements and why are these important?

## Slide 7: What is carbon footprint measurement?
Refers to the total amount of greenhouse gases (GHG) that are generated by human activity.
Potential to warm the planet once released into the atmosphere at a specific time.
Human-driven climate change

## Slide 8: What is water footprint measurement?
It measures the potential environmental impacts related to water.
Consumption or consumptive use
Water that was used by the organization, and as a result did not return to the same watershed from which it was extracted.
Water that is lost through evaporation, evapotranspiration or discharge to a different watershed.
Shortage
corresponds to
Impact category:
for example:
Degradation or degradative use
Activities that can potentially affect or worsen the water quality.
Application of products to soil and air that may reach water sources, or application of these products directly to water that may affect water quality
Eutrophication in fresh & salt water
Ecotoxicity and Human toxicity
Impact category:
for example:
corresponds to

## Slide 9: Why is it important to calculate these footprints?
Meet the demands from international markets and consumers
Opportunity to enhance input management and reduce operational costs
Reducing environmental impact of operations and increasing compliance with environmental requirements (1.5 °C target)
Enhanced brand image and reputation (product differentiation and business opportunities)
Robust information for decision-making

## Slide 10
What other benefits do you see in measuring the carbon and water footprints?

## Slide 11
What does a verifiable carbon footprint study look like?

## Slide 12
What does a verifiable carbon footprint study look like? (continued)
Define the physical areas that delimit the company
Define direct and indirect emissions and set a baseline year
Compile information
on each
emission-generating activity

## Slide 13
What does a verifiable carbon footprint study look like? (continued)

## Slide 14
What does a verifiable carbon footprint study look like? (continued)

## Slide 15
What does a verifiable water footprint study look like?

## Slide 16: Step 1. Define the objective and scope of the study
What does a verifiable water footprint study look like? (continued)
Function of the organization
Years of study
Impact category selected
Assumptions and decisions
Data and data quality
Facilities included
Study system and limits
Geographical location
Impact estimation and methodology
Expression of results
Exclusions, limitations, cut-off criteria and uncertainties

## Slide 17: Step 2. Develop and analyze the inventory
Data needed to estimate impacts (inventory)
Impact expression units
Water footprint
(impact profile)
Volume of a water lost from the watershed
Phosphorus applied to soil or discharged into freshwater
Nitrogen applied to soil or discharged into salt water
Quantity of active amount applied
Quantity of active ingredient applied
Cubic meters of water equivalent (m3e)
Kilograms of phosphorus equivalent (kg Pe)
Kilograms of nitrogen equivalent (kg Ne)
Comparative toxic ecotoxicity units (CTUe)
Comparative toxic units of human toxicity (CTUth)
Shortage
Freshwater eutrophication
Saltwater eutrophication
Ecotoxicity
Écotoxicité
Human toxicity
What does a verifiable water footprint study look like? (continued)

## Slide 18: Step 3. Assess water footprint impacts
Methodologies:
AWARE
USEtox
ReCiPe
 Shortage
© Noun Project
 Freshwater eutrophication
 Saltwater eutrophication
 Ecotoxicity
 Human toxicity
The ‘severity’ of the impacts are context specific as it depends on the water availability, types of soils and climatic characteristics of the area
What does a verifiable water footprint study look like? (continued)
Water footprint profile |  |  | 
Impact | Field | Packing house | Total
Shortage (m³e) |  |  | 
Freshwater eutrophication (kg Pe) |  |  | 
Saltwater eutrophication (kg Ne) |  |  | 
Ecotoxicity (CTUe) |  |  | 
Human toxicity (CTUh) |  |  | 

## Slide 19
3.
Measuring carbon and water footprints in the pineapple sector

## Slide 20: Measuring the carbon and water footprint in the pineapple sector
    Guide developed by the FAO Responsible Fruits Project
    Why?
    Respond to the need for measurement of footprints (prioritized by the industry) and market demand
    Provide a quantitative framework for measuring carbon and water footprints
    Enable users to measure footprints autonomously Support the reduction of environmental impacts of pineapple production and trade Optimization of processes, efficiency and cost savings
    Contribute to risk mitigation and prevention (aligned with responsible business conduct)

## Slide 21: Development of the guide
    Building on the experience of measuring carbon and water footprints in banana value chains (World Banana Forum) and adapting this to the pineapple industry.
    Based on internationally recognized methodologies (ISO 14064 for carbon and ISO 14046 for water).
    Validation with six export-oriented pineapple producing and packing companies and cooperatives in Costa Rica.

## Slide 22: Scope of carbon and water footprint measurement:
Land preparation
Bedding preparation
Sowing
Application of technological packages
Fruit reception
Fruit washing
Sorting and packaging
Refrigeration
Container loading
Transportation from the packing plant to the port
Water
footprint
Irrigation
Rain for crop hydration
Water use in fumigation mixtures and improvers
Equipment wash
Sanitary facilities
Fruit washing
Fungicide spraying
Facility cleaning
Sanitary facilities
Pediluvium (footbath)
Faucets
Dining area
Vehicle cleaning
Carbon
footprint
Processes included
Processes outside the scope of the guide
Cultivation and harvesting
Transport to port
Packing plant
Port
International shipping
Sales point
Final consumer

## Slide 23: Contents: Carbon footprint measurement guide
1
2
3
4
5
6
Carbon footprint of the company:
Carbon footprint calculation overview Scope of an emissions inventory Identification of emission sources Consolidation of carbon footprint results Emissions reduction opportunity (measures) Inventory uncertainty

## Slide 24
Example: guidance to identify and calculate GHG emissions

## Slide 25: Contents: Water footprint measurement guide
25
Water footprint of the company:
Overview of water footprint calculation
Scope of the water footprint
Water balance identification and product usage
Assessing water footprint impacts
Water footprint report
Water footprint reduction measures
1
2
3
4
5
6

## Slide 26
Example: guidance to identify and calculate the impacts on water

## Slide 27
How do you think this tool can be used in your company?

## Slide 28
5. Reducing GHG emissions and water impacts in pineapple value chains

## Slide 29: Recommendations to reduce the carbon footprint
© oun Project
Energy: Clean and well-functioning energy systems
Fuels: Efficient vehicles, optimization of routes, fuel-saving devices
Refrigerant gases and fire extinguishers: Maintenance, monitoring and replacement
Solid waste and wastewater disposal: Lower organic matter load in wastewater, water reuse & circulation, water consumption optimization, separation & recycling.
Stubble management and tillage: tillage practices with lower emissions, reincorporation of organic matter in the soil.
Inputs: Optimized use of agrochemicals, use of integrated pest and nutrition management.

## Slide 30: Recommendations to reduce the water footprint
Shortage
Degradation (quality)
Efficient irrigation technologies
Water treatment, recirculation and reuse
Rainwater harvesting
Reforestation and forest protection
Rational use of agrochemicals (integrated pest management, nutrient management)
Soil and biodiversity protection
Integrated solid waste management
Integrated liquid waste management

## Slide 31: Thank you!
https://bit.ly/responsible-fruits
Responsible-Fruits@fao.org